## Slide 1: An Experimental Doppler Study of a Table-Top Galactic Model
By: Robert Lowry and Caleb Teske

## Slide 2: Project Outline
Introduction
  Summary of Previous Project
  Motivation for Continuing Project/Problem Statement
Design & Construction of Doppler Machine
  Spinning Arm Improvements
  Motor Mount/Housing Improvements
    Angular Velocity Test Results Using Logger Pro Software
  Motor Stand/Base Improvements
Background
  General Doppler Effect
  Doppler Effect for Uniform Circular Motion
  Doppler Effect for Tilted Platform in Uniform Circular Motion
Testing/Results
  Experimental Procedure
  Spectrum Lab Results
Conclusions
Recommendations for Future Project Groups

## Slide 3: Summary of Previous Project
Doppler Machine conceived by IQP group in 2008 and described in 2009 report entitled: Ongoing Advancement of the Physics Toolbox
Equipment Used for Doppler Experiment Until C-Term 2009

## Slide 4: Motivation for Continuing Project
This project was recognized as having potential for improvement and application in future undergraduate freshmen lab experiments
To gain a deeper understanding of the meaning of the sound spectrum as observed in Spectrum Lab
Derive our own equations (which include the angle of tilt) to model the new Doppler device
Hands-On aspect of Doppler experiment with redesigned machine allows all students to learn about the Doppler effect in a new and exciting way

## Slide 5: Problem Statement/Goals
Problem Statement
While the prototype Doppler machine is an excellent starting point, in order to create a repeatable lab experiment, a new version of the Doppler device needed to be created and new data collected
Goals
To understand the observed sound spectrum
Eliminate vibration in the machine that is caused by the motor and the spinning arm, and eliminate ambient noise in the observed sound spectrum
Improve overall design of device and results to advance this project towards being ready for use in a laboratory setting

## Slide 6: Spinning Arm Improvements
Light-weight Balsa wood with tapered edges
Dual buzzer mounts which can be moved to various distances along the length of the arm
Higher quality buzzers that produce a single frequency
High quality hardware that improves balance
Emergency release set-screw

## Slide 7: Motor Mount/Housing Improvements
Redesigned with thick pine walls and plexiglass top
Rubber vibration isolation pads underneath motor and connecting motor screws to motor housing
Three large computer fans to aide in cooling
Vernier LabPro attached to housing which can be used measure angular velocity

## Slide 8: Logger Pro Results
Vernier LabPro was used to measure angular velocity for various buzzer positions (results below)
Step-by-step Logger Pro tutorial included in report
Chart: Angular Velocity vs Buzzer Radius
| 34 | 32 | 30 | 28 | 26 | 24 | 22 | 20 | 18 | 16 | 14 | 12
Angular Velocity ± 5% | 338.5676 | 357.5533 | 372.6269 | 387.4405 | 403.1112 | 430.8649 | 459.7529 | 476.3501 | 488.5989 | 512.8225 | 527.8893 | 561.7017

## Slide 9: Motor Stand/Base Improvements
Thicker plywood
Convenient On/Off Switch
Hinged platform that rotates to 90 degrees with built-in protractor
Durable metal handles for carrying and tilting
Metal rails that allow machine to slide easily on to a lab pedestal
Thumb screws for tightening the machine to the lab pedestals
Rubber vibration isolation pads to reduce vibration from motor and arm

## Slide 10: Before and After Photos
Old Machine
New Machine

## Slide 11: The Doppler Effect
Generalized Doppler Equation in 2-D: the observed
frequency f is related to the emitted frequency of the source f₀
by the equation
where ν is the velocity of waves in the medium,
νr is the velocity of the source relative to the medium and
νs is the velocity of the receiver relative to the medium
In the case of a stationary observer (or microphone), the equation reduces to
where νs is positive if the source is moving away from the observer, and negative when
moving towards the observer
These equations assume that the source is directly approaching
or receding from the observer.

## Slide 12: Doppler Equation for Uniform Circular Motion
Geometry Used to Calculate Approaching/Receding Speeds
***Derivation and Image Taken from The Doppler Effect of a Sound Source Moving in a Circle by Marcelo M.F. Saba and Rafael Antonio da S. Rosa***

## Slide 13: Doppler Equation for Tilted Platform in Uniform Circular Motion

## Slide 14: Doppler Equation for Tilted Platform in Uniform Circular Motion (cont’d)
= vs
(Plug vs into Equation 1 from Uniform Circular Motion Slide to calculate freq. shift)


## Slide 15: Experimental Procedure
Series of experiments for each parameter
  Distance
  Angular Dependence
  Tilt Dependence
  Buzzer Radius/Angular Velocity
Proper setup is important for this experiment
Results can be highly sensitive to room conditions and computer configurations
Read the full report for a detailed list of preparations that need to be made in the lab before acquiring Doppler data

## Slide 16: Spectrum Lab Results
Comparison of newly acquired data with data from
previous project group indicated:
The clarity of the observed sound signal from the new Doppler machine with the monotonic buzzers was dramatically improved
Overall noise levels in the system were greatly reduced
Doppler shifting can be observed at all different angles of tilt
The microphone receives a broad range of harmonic frequencies that need to be systematically analyzed

## Slide 17: Comparison of Results
Old Machine with Old Buzzers

## Slide 18: Comparison of Results
New Machine/New Buzzers

## Slide 19: Comparison of Results
New Machine/New Buzzers (tilted to 90⁰)

## Slide 20: Conclusions
We have gained great control over all adjustable parameters
This machine is capable of generating repeatable, reliable data under proper laboratory conditions
This experiment, if done properly, is a fun way to show a known concept in a new and exciting format
Rob is continuing this project as part of his Masters Degree, so there is plenty of time to collect more data
Analogous to planets in orbit where the source would be the light from the planets and the observer would be a telescope instead of a microscope

## Slide 21: Recommendations
Conduct testing with lower frequency buzzers for more dramatic effects
Move a computer to the attic and spend more time collecting data in the Anechoic Chamber
Derive equations to calculate the harmonic properties of the buzzers and analyze intensity distribution
Consider using different batteries that would take up less space