## Slide 1: Assessment of Green Hill Park Ponds’ Water Quality
By Aaron Swann, Cyril Ogbebor, and Gabe Buziba

## Slide 2: Acknowledgements
Brian McCarthy (Sponsor & President of GHPC)
Members of GHPC
Prof. Roberts (Project Advisor)
Jacquelyn Burmeister (Senior Environmental Analyst)
Robert Antonelli (Assistant Commissioner of DPW&P)
David Harris (Assistant Director Sewer Operations)
Ian Weyburne (Sanitary/Stormwater Engineer)
Prof. Walker
Prof. Sakulich
Prof. Mathisen
Donald Pellegrino (CEE Lab Manager)

## Slide 3: Background
Largest in the City of Worcester
Almost 500 acres
Golf course, skate park, farm, and two ponds
Pond was created by Martin Green in 1878
The City of Worcester acquired the park in 1905

## Slide 4: Background (Cont’d)
Green Hill Park Coalition
Created in 2000
Main goals: Preserving the remaining acreage, enhancing the park and protecting the park

## Slide 5: Project Motivations
Degrading Pond water quality
Effects of an Irrigation system

## Slide 6: Goal 1: Condition of the Pond
Objective 1: Study the Baseline
Objective 2: Investigate Pollutant Sources
Objective 3: Research Mitigation Against Contaminants

## Slide 7: Nashoba Test Results
Routine Water Testing Results |  |  |  |  |  |  |  |  |  |  |  | 
Parameter & Units | June 10th 2022 |  | May 24th 2022 |  | April 28th 2022 |  | June 15th 2021 |  | October 19th 2020 |  | MRL | MCL
 | GHPL | GHPO | GHPL | GHPO | GHPL | GHPO | GHPL | GHPO | GHPL | GHPO |  | 
E. Coli, /100ml | - | - | - | - | 3 | 8 | 58 | 58 | PRESENT | PRESENT | 1 | -
Total Coliform Bacteria, /100ml | >2420 | >2420 | >2420 | 1120 | 727 | 517 | 440 | 260 | PRESENT | PRESENT | 1 | Absent
Iron, MG/L | 0.191 | 0.382 | 0.102 | 0.314 | 0.076 | 0.405 | 0.154 | 0.135 | 0.158 | 0.291 | 0.004 | 0.3
Manganese, MG/L | 0.08 | 0.067 | 0.095 | 0.068 | 0.052 | 0.065 | 0.041 | 0.038 | 0.101 | 0.019 | 0.004 | 0.05
Sodium, MG/L | 36.7 | 16.6 | 36.5 | 16.8 | 34 | 14.2 | 36.5 | 36 | 39 | 10.9 | 0.2 | 250
Chloride, MG/L | 67.5 | 44.7 | 71.1 | 46.6 | 68.2 | 39.8 | 68.1 | 67.3 | 75.8 | 20 | 1 | 250
Color Apparent, CU | 25 | 30 | 15 | 30 | 8 | 18 | 35 | 35 | 5 | 25 | 0 | 15
Odor, TON | 1 | 2 | 3 | 4 | 1 | 1 | 0 | 0 | 1 | 2 | 0 | 3
pH at 25C | 7.7 | 6.3 | 6.6 | 6 | 6.6 | 6.1 | 8.6 | 8.9 | 6.7 | 6.5 | NA | 6.5-8.5
Sulfate, MG/L | 7.4 | 6.4 | 7.3 | 7.1 | 7.4 | 7.4 | 7.8 | 8 | 9.1 | 8.3 | 1 | 250

## Slide 8: Metal Contaminants

## Slide 9: Total Coliform

## Slide 10: Cyanobacteria
Risk for Bloom | Phycoyanin Concentration (ug/l) | Particle Concentration (#/ml) | Cyanobacteria Presence | Cyanobacteria Character
June 2021 | - | 3786 | - | Trichrome, Ceratium
July 2021 | 21 | 1792 | - | Microcystis, Anabaena
October 2021 | - | - | Low | Woronichinia, Dolichospermum
May 21st, 2022 | 10 | 3367 | Some | Aphanizomenon
Almost None | 0-15 | 0-1000 | None | -
Low | 15-20 | 1000-5000 | Low | -
Elevated | 20-50 | 5000-10000 | Some | -
Blooming | >50 | >10000 | High | -

## Slide 12: Water Sample Locations for Water Analysis at WPI Lab

## Slide 13: WPI Test Results
GHPL
GHPO

## Slide 14: Total Phosphorus Concentration in the Ponds
Sample Location | Absorbance | Concentration
1 | 0.034 | .115ppm
2 | 0.039 | .137ppm
3 | 0.069 | .27ppm
4 | 0.026 | .081ppm
5 | 0.032 | .11ppm

## Slide 15: Dissolved Oxygen Level in Both Ponds
GHP-1 |  | 11.2 MG/L
GHP-3 |  | 11.55 MG/L
GHP-5 |  | 12.25 MG/L

## Slide 16: Goal 2: Feasibility of Pond Irrigation
Objective 1: Determine the Volume of the Pond
Objective 2: Compare the Incoming and Outgoing Water

## Slide 17: Irrigation Methods
Volume: Area x Depth
Water Entering: Springs and Rainwater
Water Exiting: Drain, Evaporation, and Irrigation

## Slide 18: Irrigation Methods (Cont'd)
Area: 30 acres
Average Depth: 7.32 ft
Volume: 219.54 acre-ft or About 71.5 Million Gallons
Average Summer Rainfall: 12.8 Million Gallons Per Month
Average Summer Irrigation: 11.8 Million Gallons Per Month
Pond Loses 9.5-10 Million Gallons Per Foot Due to Evaporation

## Slide 19: Recommendations
Vegetative Buffer
Treatment Options
Do Not Implement Irrigation System

## Slide 20: Vegetative Buffers
Intercept, retain and transform pollutants contained in flowing water
Examples of Vegetative Buffers:
Vetiver grass
Switch grass
Side Oats Grama Grass
Big Bluestem Grass
Little Bluestem Grass

## Slide 21: Treatment
Proactive
  Aluminum Sulfate
  Copper Sulfate
  Cutrine Plus
Services
  Solitude Lake Management

## Slide 22: Irrigation Issues
Cyanobacteria is an issue
Evaporation was an unknown variable

## Slide 23: Irrigation Benefits
Saving Resources
Saving Money
Limiting the Potential Chemical Impact

## Slide 24: Irrigation Possibilities
Modifications to the Flow System of the Pond
Keep a Record of Water Level Fluctuations
Irrigation System Can Only be Considered After the Cyanobacteria Issue is Solved

## Slide 25: Thanks For Your Time! Any Questions?