## Slide 1
Sensor and Servo Enhanced Smart Arm Cast
Aedan Fahy(ME), Achilles Gikas(ME/BME), Shawn Mills(ME/BME), Shaniqua Miller(ME)
Mechanical and Materials Engineering Department
OBJECTIVES
MOTIVATION
ACKNOWLEDGEMENTS
I: Ideate a potential product that serves as a smart wearable device for consumers
II: Design a model with the use of mechanical equipment and engineering principles
III: Develop the model to create a functional prototype of the smart wearable cast
IV: Test, analyze results, redesign, and redevelop the product for improvement
Arm fracture cases are expected to increase to over 3 million by 2025
Current casting processes use skin-irritating and non-reusable material
Cast applications require tedious multi-step methods
The healthcare industry lacks smart devices accessible to patients
Sensor-based technology will efficiently and effectively fixate an injured wrist autonomously
FUTURE WORK AND CONCLUSIONS
REFERENCES
[1] N. N. O’Hara, D. S. Kringos, G. P. Slobogean, Y. Degani, and N. S. Klazinga, “Patients Place More of an Emphasis on Physical Recovery Than Return to Work or Financial Recovery,” Clin Orthop Relat Res, vol. 479, no. 6, pp. 1333–1343, Jun. 2021.
[2] A. M. Gordon, A. T. Malik, and K. S. Goyal, “Trends of hand injuries presenting to US emergency departments: A 10-year national analysis,” Am. J. Emerg. Med., vol. 50, pp. 466–471, 2021
[3] R. Huggenberger and M. Detmar, “The Cutaneous Vascular System in Chronic Skin Inflammation,” J Investig Dermatol Symp Proc, vol. 15, no. 1, pp. 24–32, Dec. 2011.
[4] T. Xu, W. Shen, X. Lin, and Y. M. Xie, “Mechanical Properties of Additively Manufactured Thermoplastic Polyurethane (TPU) Material Affected by Various Processing Parameters,” Polymers, vol. 12, no. 12, 2020
TESTING AND RESULTS
Our project team conducted work throughout the academic year alongside our Mechanical Engineering advisor, Professor Mehul Bhatia Ph.D. Our additional project co-advisor from the Biomedical Engineering Department is Professor Songbai Ji Ph.D. We are also grateful to conduct work using resources from the MQP Laboratory with the help of James Van Mulligan.
CAST MATERIAL AND DESIGN MODELING
Doctor applying short arm cast to a patient
PROJECT ADVISOR: Mehul Bhatia Ph.D
PROJECT CO-ADVISOR: Songbai Ji Ph.D
CAST SENSORS AND EQUIPEMENT
Process of Arduino Code:
Establish baseline pressure for the patient from initial strain gauge readings
Calculate the Avg Heart Rate of the patient via Pulse Oximeter
If below or above normal/walking range (65-90 bpm) servo motor tightens or loosens cast respectfully
If the button is pressed, the strain gauge takes readings
Servo Motor adjust is strain gauge measures too loose or too tight
LCD displays avg Heart Rate and how much the Servo motor needs to move (if needed)
Repeat the loop from step 2
Testing after assembly and wiring included:
Calibration Strain Gauges, Servo Motor, and Pulse Oximeter
Baseline Test on Patient's Arm to maintain pressure over a period of time (1 hour)
Testing of Pulse Oximeter Detecting High and Low Heart Rate and Loosening or Tightening of baseline pressure respectfully
Testing of Baseline Pressure deviation detection from Strain Guage and adjustment from servo motor
ARDUINO WIRING AND CODING
Figure 1: Final CAD cast Assembly in SolidWorks
Thermoplastic Polyurethane (TPU) is the protective layer that makes up the main body of the cast.
- TPU properties:
- Very ductile (E = 2.58 GPa)
- Durable and hard (66.3 R)
- Low density (1.45 g/cc)
TPU filament was used in 3D printing applications to create the structure
  TPU applications:
    Engineering
    Sports Equipment
    Medical Devices
Electrical Equipment used along with their purpose:
Arduino Nano r3: Central Brain to calculate Pressures and send electrical signals to equipment
Strain Guage (x2): Calculate the pressure cast is putting on the patient's arm
MAX30102 Pulse Oximeter: Calculate the average heart rate of the patient to determine the high or low activity for the servo to adjust accordingly
LCD Display: Displays Heart rate and tightness
Tower Pro Servo Motor: Tightens or loosens cast through a network of nylon wire across the cast
Momentary Circuiting Button: Sends signal to Arduino to activate the strain gauge
10k ohm Potentiometer: Set the source of the LCD text brightness for the patient
4.2 V Battery: Power source of wiring
Figure 5: Fritzing Diagram of System
Figure 2: Isometric View of Cast in SolidWorks
Figure 6: Photograph of assembled Smart Arm Cast with wires exposed
Testing after assembly and wiring included:
LCD Display needed adjustment from potentiometer
Adjustment needed long period to tighten
Loosening of cast felt more jolted than tightening procedure
Figure 3: Bottom-Left View of Cast in SolidWorks
The main body of the arm cast was designed using the computer-aided design (CAD) software SolidWorks
To create the model, measurements were taken of the cross-sectional diameter of both the wrist and the end of the forearm on a team member’s body
The wrist diameter measures at 54mm
The elbow diameter measures at 97mm
The length of the cast measures at 6 inches
The overall thickness of this layer to ensure protection and fixation of the patient’s arm is 6 millimeters
Figure 4: Exploded View of Cast Assembly
Figure 7: Proposed CAD Model of Hand Section
Fabricate a third layer to protect and conceal the wiring and electronics.
Fabricate the hand section so the cast can provide proper fixation of the wrist.